## Slide 1: Design and Simulation of Digital Even and Odd Parity Generator Using XOR Gates
Project Title: Digital Even and Odd Parity Generator Using XOR Gates
Team Members & Roll Numbers: Vineeth-2620080042
Sreekar-2620030478
Manideep-2620030406
Ariharasudhan-2620030482
Guide: Dr Venkat Isampalli
Department of Electronics Engineering
Academic Year: 2026–27

## Slide 2: Introduction
Digital data can be corrupted by noise during transmission.
A parity bit is an extra bit added to data to help check data integrity.
This project demonstrates even and odd parity generation using cascaded XOR gates.
The circuit is tested through digital logic simulation.

## Slide 3: Objectives
Design even and odd parity generators using XOR gates.
Understand how XOR gates determine parity.
Generate the required parity bit for a given binary input.
Simulate and verify the circuit using Logisim.

## Slide 4: Course Outcomes (COs)
CO1: Explain the role of parity in digital data communication.
CO2: Apply XOR logic to generate parity bits.
CO3: Develop a cascaded XOR logic circuit.
CO4: Simulate and verify circuit outputs using Logisim.
CO5: Identify applications and limitations of parity-based error detection.

## Slide 5: Components Required
Digital input bits (D₃, D₂, D₁, D₀)
XOR logic gates
Logic circuit simulator (Logisim)
Output indicator / LED (for observing the parity output)
Connecting wires and power source, as required by the implementation

## Slide 6: Block Diagram
Binary Input Data → Cascaded XOR Gates → Parity Output (P)
The input bits are fed into a chain of XOR gates.
The final output indicates whether the input contains an odd or even number of 1s.
The parity bit can then be appended to the original data.

## Slide 7: Circuit Working
The input data bits are applied to the XOR network.
Each XOR gate outputs 1 when its two inputs are different.
The cascaded XOR output is 1 when the input contains an odd number of 1s.
For even parity, use this output as the parity bit; for odd parity, use its complement.

## Slide 8: Truth Table
XOR Gate: A ⊕ B
A = 0, B = 0 → Output = 0
A = 0, B = 1 → Output = 1
A = 1, B = 0 → Output = 1
A = 1, B = 1 → Output = 0
For input 1011, there are three 1s, so the XOR cascade output is 1.

## Slide 9: Logic Design
XOR cascade: X = D₃ ⊕ D₂ ⊕ D₁ ⊕ D₀
Even parity bit: Pₑ = X
Odd parity bit: Pₒ = NOT X
For input 1011, X = 1.
Therefore, even parity bit = 1 and odd parity bit = 0.

## Slide 10: Simulation / Implementation
Build the cascaded XOR circuit in Logisim.
Apply the test input D₃D₂D₁D₀ = 1011.
Calculate the output: 1 ⊕ 0 ⊕ 1 ⊕ 1 = 1.
Verify that the even parity output is 1 and the odd parity bit is 0.
Observe the output indicator to confirm the result.

## Slide 11: Advantages
Simple circuit with a small number of logic gates.
Fast and easy to implement.
Low-cost method for basic error detection.
Useful for learning XOR gates and digital circuit simulation.
Can be applied to both serial and parallel data systems.

## Slide 12: Limitations
Parity cannot identify which bit is corrupted.
It cannot detect every multiple-bit error pattern.
It does not correct errors by itself.
Stronger methods, such as Hamming codes or CRC, may be needed for improved error detection.

## Slide 13: Applications & Future Scope
Error detection in data communication links.
Basic error-checking in computer networks and memory systems.
Teaching digital logic and XOR gate applications.
Future scope: extend the design to more input bits or combine it with stronger error-detection methods.

## Slide 14: Conclusion
An even and odd parity generator was designed using cascaded XOR gates.
The circuit produces a parity output based on the number of 1s in the input.
The input 1011 gives an XOR output of 1, resulting in even parity bit 1 and odd parity bit 0.
The project demonstrates a simple digital method for checking data integrity.

## Slide 15: Project Files / Simulation
Simulation tool: Logisim
Suggested project materials:
• Circuit diagram of the cascaded XOR network
• Logisim circuit file
• Test cases and observed outputs
• Project report and presentation
GitHub Repository link -
https://github.com/neelamsreekar-123/PARITY-GENERATOR

## Slide 16: Thank You